## Slide 1
K L Deemed to be University
Department of Computer Science and Engineering | DDCA
Module 2
Combinational Logic & ALU
Digital Design & Computer Architecture | 26EC1202E
2026 - 2027 (Odd Sem)

## Slide 2: Module 2 Overview
INTRO
1
Combinational Logic
2
Karnaugh Maps (K-maps)
3
Half Adder & Full Adder
4
Ripple-Carry Adder
5
Two's-Complement Subtraction
6
Adder / Subtractor
7
Multiplexer & Decoder
8
Comparator
9
ALU: the CPU's Calculator
The ALU is the first major CPU subsystem we build: it performs arithmetic and logical operations on data.

## Slide 3: Combinational Logic
FOUNDATIONS
No memory
Output depends only on the current inputs.
Built from gates
Made entirely of logic gates.
Examples
Adders, subtractors, MUX, decoder, comparator, ALU.
Inputs
(A, B, ...)
Combinational
Logic Circuit
Outputs
(Y, ...)

## Slide 4: Karnaugh Maps (K-maps)
FOUNDATIONS
Simplifies Boolean expressions
Reduces the number of gates
Leads to minimal, efficient circuits
Simplified expression
F = C + A′B
Example: F(A,B,C) = Σm(1,2,3,5,7)
00
01
11
10
A \ BC
0
0
1
1
1
1
0
1
1
0
Group 1 (quad): C
Group 2 (pair): A′B
Notes: Corrected from the original: F = C + A'B for minterms 1,2,3,5,7.

## Slide 5: Half Adder & Full Adder
ARITHMETIC
Half Adder
Adds two 1-bit inputs; outputs Sum and Carry.
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Sum = A ⊕ B Carry = A · B
Full Adder
Adds three 1-bit inputs (A, B, Cin); outputs Sum and Carry.
A | B | Cin | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Full adder row 011 Sum corrected to 0.

## Slide 6: Ripple-Carry Adder
ARITHMETIC
Cascades full adders
Carry moves from LSB to MSB
Used for multi-bit addition
Cin
A₀
B₀
FA
Cout
S₀
A₁
B₁
FA
Cout
S₁
A₂
B₂
FA
Cout
S₂
A₃
B₃
FA
S₃

## Slide 7: Two's-Complement Subtraction
ARITHMETIC
1
Invert B
2
Add 1 to get B′ + 1
3
Add the result to A
A − B = A + (B′ + 1)
The same adder circuit can be reused.
Example: 5 − 3 (4-bit)
5 = 0101
3 = 0011
3′ = 1100, +1 = 1101
0101 + 1101 = 10010
Discard carry: 0010 = 2

## Slide 8: Adder / Subtractor
ARITHMETIC
0
M = 0 → Addition
1
M = 1 → Subtraction (B inverted, Cin = 1)
Cin = M
B₀
A₀
⊕
M
FA
S₀
B₁
A₁
⊕
M
FA
S₁
B₂
A₂
⊕
M
FA
S₂
B₃
A₃
⊕
M
FA
S₃

## Slide 9: Multiplexer (MUX)
DATA HANDLING
Selects one input using the select lines
Commonly used for data routing
MUX
2:1
I₀
I₁
Y
S
S | Y
0 | I₀
1 | I₁
Y = S′·I₀ + S·I₁

## Slide 10: Decoder
DATA HANDLING
Converts an n-bit input into up to 2ⁿ outputs
Only one output is active at a time
2-to-4
Decoder
A
B
Y₀
Y₁
Y₂
Y₃
A | B | Y₀ | Y₁ | Y₂ | Y₃
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Notes: Corrected: n-bit input gives up to 2^n outputs (original said 2^m).

## Slide 11: Comparator
DATA HANDLING
Compares two n-bit numbers
Outputs: A > B, A = B, A < B
A[n-1:0]
B[n-1:0]
Comparator
A > B
A = B
A < B

## Slide 12: ALU: the CPU's Calculator
THE ALU
Performs arithmetic and logical operations
Takes two inputs and a control signal
Outputs a result and status flags
A
B
Control
ALU
Result
Flags (Z, C, N, V)
Z
Zero
C
Carry
N
Negative
V
Overflow

## Slide 13: ALU Design & Verification in Logisim
THE ALU
1
Build each block separately (adder, MUX, decoder)
2
Combine into the ALU using control signals
3
Test with different inputs and verify outputs
Suggested ALU operations
Addition (A + B)
Subtraction (A − B)
AND (A & B)
OR (A | B)
XOR (A ^ B)
NOT (~A)
Set less than (A < B)
Pass-through

## Slide 14: Conclusion
WRAP-UP
1
Combinational logic forms the foundation of the CPU
2
K-maps help simplify logic circuits
3
Adders, subtractors, MUX, decoder and comparator are key building blocks
4
The ALU combines these to perform real CPU operations
Next step: implement and test the ALU in Logisim / Digital simulator.

## Slide 15: References
WRAP-UP
1
Course Handout: DDCA (Module 2)
2
Logisim / Digital Documentation
3
RISC-V Architecture (for context)
“Logic builds the circuits,
Circuits build the machine.”

## Slide 16
Thank You!
Any Questions?