## Slide 1
1+1=10 0+1=1 1+0=1 0+0=0
1+0=1 0+0=0 1+1=10 0+1=1
1+1=10 0+1=1 1+0=1 0+0=0
1+0=1 0+0=0 1+1=10 0+1=1
1+1=10 0+1=1 1+0=1 0+0=0
A
B
Σ
C
DIGITAL DESIGN & COMPUTER ARCHITECTURE
Half Adder and Full Adder
Building Blocks of Binary Addition
Mini Project — DDCA Course

## Slide 2
Objective
What this project sets out to do
1
Understand the building blocks
See how binary addition is done at the gate level, one bit at a time.
2
Design a half adder
Build the two-input circuit that adds a single pair of bits.
3
Design a full adder
Extend it with a carry-in so multi-bit addition becomes possible.
4
Chain them together
See how full adders combine into a ripple-carry adder.
2
inputs (A, B) — Half Adder
3
inputs (A, B, Cin) — Full Adder
A full adder accepts a carry-in — a half adder cannot.
DDCA — Half Adder & Full Adder
2

## Slide 3
Half Adder — The Concept
Definition
A half adder adds two single binary digits, A and B, and produces a Sum and a Carry.
Sum = A ⊕ B
Carry = A · B
XOR gives the sum bit (1 when inputs differ); AND gives the carry bit (1 only when both inputs are 1).
Truth Table
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Only one row produces a carry (1+1) — this is where the third input of a full adder becomes necessary.
DDCA — Half Adder & Full Adder
3

## Slide 4
Half Adder — Circuit Design
Two gates, two outputs — Sum from XOR, Carry from AND
Input A
Input B
XOR Gate
AND Gate
Sum
(A XOR B)
Carry
(A AND B)
1
The XOR gate produces the sum bit — it outputs 1 only when A and B are different.
2
The AND gate produces the carry bit — it outputs 1 only when both A and B are 1.
3
Limitation: with no carry-in pin, half adders can't be chained for multi-bit addition.
DDCA — Half Adder & Full Adder
4

## Slide 5
Full Adder — Why We Need It
Multi-bit addition needs a way to pass carries forward
1
The problem
When adding numbers with more than one bit, each column may produce a carry that the next column must add in.
2
The gap
A half adder only has two inputs (A, B) — there's no pin for an incoming carry from the previous column.
3
The fix
A full adder adds a third input, Cin, so it can accept the carry from the column before it.
4
The payoff
Because it accepts and produces a carry, full adders can be chained — one per bit — to add numbers of any width.
A
B
Cin
Full
Adder
Sum + Cout → next column
DDCA — Half Adder & Full Adder
5

## Slide 6
Full Adder — Truth Table
All 8 combinations of A, B and Cin
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Sum = A ⊕ B ⊕ Cin Cout = AB + Cin(A ⊕ B)
DDCA — Half Adder & Full Adder
6

## Slide 7
Full Adder — Built from Two Half Adders
A common, reusable way to construct the full adder circuit
A
B
Half Adder 1
Sum1
Carry1
Cin
Half Adder 2
Sum (final)
Carry2
OR Gate
Cout
1
Half Adder 1 adds A and B, giving a partial sum (Sum1) and a carry (Carry1).
2
Half Adder 2 adds Sum1 to Cin, giving the final Sum and a second carry (Carry2).
3
Since Carry1 and Carry2 can never both be 1 at once, an OR gate safely combines them into Cout.
DDCA — Half Adder & Full Adder
7

## Slide 8
Worked Example — 4-bit Ripple Carry Addition
0111 (7) + 0011 (3), one full adder per bit position
Bit | A | B | Cin | Sum | Cout
0 (LSB) | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1
2 | 1 | 0 | 1 | 0 | 1
3 (MSB) | 0 | 0 | 1 | 1 | 0
Carry-in of the LSB stage is 0 (nothing to carry into the first column); each stage's carry-out feeds the next stage's carry-in.
Sum bits (MSB→LSB) = 1 0 1 0 = 1010₂ = 10₁₀ (7 + 3 = 10 ✓)
DDCA — Half Adder & Full Adder
8

## Slide 9
Comparison & Applications
Half Adder
2 inputs (A, B), 2 outputs (Sum, Carry).
Built from one XOR gate and one AND gate.
No carry-in — can only be used for the least-significant bit.
Simple, but not enough on its own for multi-bit addition.
Full Adder
3 inputs (A, B, Cin), 2 outputs (Sum, Cout).
Built from two half adders plus an OR gate.
Accepts a carry-in, so it can be chained across bit positions.
The basic unit of ripple-carry adders and ALUs.
Where they're used: ripple-carry and carry-look-ahead adders, ALUs in processors, binary counters, and any digital circuit that performs arithmetic.
DDCA — Half Adder & Full Adder
9

## Slide 10
1
0
1
Conclusion
A half adder was designed using an XOR gate (Sum) and an AND gate (Carry), covering single-bit addition without a carry-in.
A full adder was designed by combining two half adders and an OR gate, adding support for a carry-in.
Chaining full adders bit by bit builds a ripple-carry adder, verified with a worked example: 0111 (7) + 0011 (3) = 1010 (10).
These circuits are the foundation of arithmetic in digital systems, from simple counters up to a processor's ALU.
References: M. Morris Mano, Digital Design (Pearson); Patterson & Hennessy, Computer Organization and Design; DDCA course notes; Logisim documentation.
DDCA — Half Adder & Full Adder
10